## Slide 1
Resistor Value Identifier
Choose the bands. Read the value.
A hands-on tool for selecting resistor bands and reading the resulting resistance.
4-band
5-band
Live value + tolerance
THE MANUAL CALCULATOR

## Slide 2
RESISTOR VALUE IDENTIFICATION / 01 / 07
Introduction
AI Resistor Value Identification is a project designed to identify the resistance value of a resistor using its color bands. Resistors commonly use color bands to represent their resistance and tolerance, but reading these bands manually can sometimes be difficult or time-consuming. This project provides a digital solution where users can select resistor bands and instantly obtain the resistance value and tolerance. It also includes an optional AI-based image recognition feature for identifying resistor values from photographs.

## Slide 3
02 / MAIN FEATURE
Manual calculator: from bands to a value
3 / 7
1
Choose band count
Select a 4-band or 5-band resistor.
2
Set each color
Use the labeled selectors; the resistor preview updates.
3
Read the result
Resistance in ohms and tolerance recalculate immediately.
4-band: 2 significant digits • 5-band: 3 significant digits

## Slide 4
03 / CALCULATOR EXAMPLES
Change the bands; the decoded value follows
4 / 7
RED • RED • BROWN • GOLD
YELLOW • VIOLET • RED • GOLD

## Slide 5
04 / HOW THE CALCULATOR WORKS
Digits, multiplier, tolerance
5 / 7
4-BAND RESISTOR
RED 2
RED 2
BROWN ×10
GOLD ±5%
(22) × 10 = 220 Ω
5-BAND RESISTOR
YELLOW 4
VIOLET 7
RED 0
BROWN ×10
GOLD ±5%
(470) × 10 = 4.7 kΩ
Why tolerance matters
Gold indicates ±5%; silver indicates ±10%. Metallic colors are not valid significant digits.
4-band formula: (10 × first digit + second digit) × multiplier

## Slide 6
05 / PROJECT RESULTS
A practical resistor calculator with an AI extension
6 / 7
MANUAL CALCULATOR
4-BAND / 5-BAND
220 Ω 4.7 kΩ
Decoded values with tolerance, updated from color selections.
WORKING FEATURES
• Select four or five bands • See a resistor preview • Decode resistance and tolerance • Upload-photo AI mode is optional
AI MODEL SUPPORT
• 37 resistor classes • 91% top-1 test accuracy • 99.7% top-5 on 289 held-out photos • Model/band conflicts are flagged
TAKEAWAY
The manual calculator is the core; image recognition adds a second way to identify a resistor.

## Slide 7
RESISTOR VALUE IDENTIFICATION / 07 / 07
Conclusion
The AI Resistor Value Identification project provides a practical and user-friendly way to determine resistor values. The manual calculator successfully supports both 4-band and 5-band resistors, displaying resistance and tolerance based on the selected colors. The project also includes an AI extension for image-based identification, providing an additional way to recognize resistor values. Overall, the system combines traditional resistor color-code calculation with AI-based recognition to make resistor identification faster and easier.